## Slide 1
Optimization of Hybrid Renewable Energy System (HRES) for a Remote Area in Bangladesh
Sk Asad Al Abir (200021331)
Pushpita Khan (200021354)
K.M. Sirazul Monir (200021247)
by
Supervisor: Hasan Jamil Apon
EEE 4800

## Slide 2
  Current Scenario
  Accessibility Issues in Remote Areas
  Problem Statement
  Proposed Solution
  Background and Motivation
  HOA
  Literature Review
  HOA Overview
  System Overview
  Results
  Complex Engineering Aspects
  Social, Environmental & Ethical Impact
  References
Table of Contents
7
8
9
11
13-16
43
12
39-41
24-34
35-38
3
5-6
17-23
  Introduction
1

## Slide 3
Introduction
1
  Rapid increase in electricity demand.
  Limited access of the remote areas to national grid.
Problems
  Heavy dependance on fossil fuel.
  Low renewable adoption
Motivation
  Developing a cost-efficient, sustainable and reliable project.
  A Hybrid Renewable Energy System (HRES) incorporating solar, wind, biomass and battery storage.
Context

## Slide 4
Energy Sources
Source: SREDA
2

## Slide 5
  Total power generation capacity 28,166 MW (approx).
  Peak demand 17,200 MW.
  Annual energy demand is rising by 10–12%.
  Bangladesh targets 34,000 MW capacity by 2030.
Current Scenario
3

## Slide 6
Challenges & Risks
Nationwide
Remote Area
  Grid failures despite surplus capacity.
  Heavy reliance on fossil fuels.
  Import dependance.
  Limited grid access.
  High Dependance on Kerosene and Diesel.
  Energy poverty.
4

## Slide 7
Accessibility Issues in Remote Areas
Rangamati
Khagrachhari
Bandorban
Chittagong Hill Tracts (CHT)
  Population: ~0.8 million
  Electricity Access: 60-70%
  Underserved Areas: Remote hilly regions
  Population: ~1.2 million
  Electricity Access: 85%
  Underserved Areas: Remote hilly areas
  Population: ~0.4 million
  Electricity Access: 50-60%
  Underserved Areas: Mountainous regions
5

## Slide 8
  1.6 million people
  More than 10 indigenous ethnic groups
  13,295 square kilometers
  10% of Bangladesh’s total land area
Accessibility Issues in Remote Areas
  More than 30% of villages in the region are accessible only by foot or waterways
6

## Slide 9
Problem Statement
  1.6M+ people live in CHT; many lack reliable electricity
  30%+ villages not connected to the grid (hilly terrain, cost)
  Diesel generators are costly, polluting, and unreliable
  National electrification ≠ actual rural access in CHT
7

## Slide 10
Proposed Solution
Hybrid Renewable Energy System,
optimized with
Hippopotamus Algorithm
  Smarter sizing of components
  Efficient use of local energy resources
  Minimization of cost and energy losses
Hippopotamus Optimization Algorithm
8

## Slide 11
Background & Motivation
4–6.5 kWh/m²/day
Wind: >4 m/s
Abundant rice husk
A Hybrid Renewable Energy System (HRES) can provide:
  Continuous and clean power
  Cost savings over diesel-based systems
  Environmental benefits (reduced CO₂ emissions)
9

## Slide 12
Goals and Objectives
Design & optimize cost-effective HRES
  Assess feasibility in remote areas
  Model PV, wind, biomass, battery systems
  Use HOA for optimal sizing
  Minimize cost, ensure reliability
  Analyze social & environmental impact
Primary Objective
Secondary Objective
10

## Slide 13
Hippopotamus Optimization Algorithm
Load Demand
Component Costs
Hippopotamus
Algorithm
Optimal Sizes of PV, Wind, Biomass & Battery
Minimize Cost & Ensure Reliable Power Supply
11

## Slide 14
Chowdhury et al. (2012): Proposed hybrid PV-wind-biogas system for rural areas
Amiri et al. (2024): Introduced Hippopotamus Optimization Algorithm for engineering design
Literature Review
[1]
[2]
Ullah et al. (2012): Grid-connected hybrid system model for energy resilience
[3]
Halder et al. (2015): Quantified biomass-to-electricity potential of 373 TWh/year
[4]
Title: Present scenario of renewable energy in Bangladesh and a proposed hybrid system to minimize power crisis in remote areas
Title: Hippopotamus optimization
algorithm: a novel nature‑inspired
optimization algorithm
Title: Current Status of Renewable Energy Sector in Bangladesh and a Proposed Grid Connected Hybrid Renewable Energy System
Title: Energy scarcity and potential of renewable energy in Bangladesh
12

## Slide 15
System Optimization Strategy
Position Updating in Rivers/Ponds (Exploration Phase):
  Hippos move within their territory to explore the solution space.
  The best-performing hippo leads the movement.
  Distinct models for male, female, and immature hippos ensure diverse exploration.
Defensive Strategies Against Predators (Exploration Phase):
  Hippos coordinate defensive actions to escape poor solutions.
  Helps avoid local optima and enhances exploration.
Evasion Methods (Exploitation Phase):
  Hippos make quick, localized movements to exploit optimal solutions.
  Focuses on refining and improving the best-found positions.
Phase-1
Phase-2
Phase-3
1
13

## Slide 16
Visual Representation
Phase 2: Defensive Strategies Against Predators (Exploration)
14

## Slide 17
Visual Representation (Cont.)
Phase 3: Evasion Method (Exploitation)
15

## Slide 18
Performance and Application
Goal
Strengths
Modifications
  Find the optimal solution by improving candidate solutions (hippopotamus population).
  Similar to PSO and GWO.
  Balances exploration and exploitation effectively.
  Outperforms other algorithms in performance and stability.
  Variants like MHO and IHO enhance performance.
  Incorporate chaotic maps and adaptive mechanisms.
16

## Slide 19
System Overview Diagram
17

## Slide 20
Proposed HRES Components
Solar PV Cell
Windmill
Biomass
Battery Storage
18

## Slide 21
Mathematical Modeling (PV System)
Where,
  Voc =Open Circuit Voltage
  Isc = Short Circuit Current
  Ns= Number of PV modules in series
  Np= Number of PV module in parallel
  NCOT=Nominal Cell Operating Temperature
  G_Stc= Solar Irradiance at Standard Test Condition
  FF= Fill Factor
  Kv=Open Circuit Voltage Temperature Coefficient
  Ki= Short Circuit Current Temperature Coefficient
19

## Slide 22
Mathematical Modeling (Wind & Biomass)
20

## Slide 23
Battery Storage & Load Profile
21
Fig: Hourly Load Profile

## Slide 24
Data Collection Sources
Solar Irradiance (W/m²)
Collected from PVGIS
Used to estimate daily solar power generation
Wind Speed (m/s)
Also sourced from PVGIS
Used to calculate wind turbine power output
Ambient Temperature (°C)
Required for computing PV parameters like
Open Circuit Voltage (Voc) and Short Circuit Current (Isc)
Load Demand (kWh/day)
Provided by Dohazari 132/33 KV Grid substation
Reflects actual energy consumption needs
22

## Slide 25
Simulation Steps
23
Start/Parameter Setup
Input Battery Parameters
Input biomass, PV, Wind & Cost Parameter
Load Solar, Wind & Load Profile Data
Compare Generation with Load Demand
If Generation ≥ Load → Supply Load
Charge Battery (if not full), else Dump Excess Power
If Generation < Load → Discharge Battery (if not empty)
1.
2.
Update Battery State of Charge (SOC) & Apply Self-Discharge
Perform Cost Calculations (Battery, PV, Wind, Biomass, System Total)
Display Results (Performance + Cost Analysis)
If Battery Empty → Record Power Shortage
Calculate Biomass Energy & Power Output
Calculate PV Power Output
Calculate Wind Power Output
Compute Total Generation (Hourly)
3.
4.

## Slide 26
Results
Output of the Optimization Algorithm
24

## Slide 27
Results
Effect of Search Agents on Cost Optimization
25

## Slide 28
Results
Effect of Search Agents on Cost Optimization
  Increasing search agents and iterations lead to longer simulation times.
  Total cost decreases with more search agents and iterations, indicating improved optimization.
  LCOE (Levelized Cost of Energy) decreases from 5.98 BDT/MWh (8 agents) to 5.63 BDT/MWh (64 agents), showing better cost efficiency.
26

## Slide 29
Results
Statistical Analysis
27

## Slide 30
Results
Statistical Analysis
  Total Cost: Mean of 1.15 billion BDT, with a standard deviation of 203.58 million BDT, indicating fluctuation due to stochastic factors. Range: 1.15 billion to 2.04 billion BDT.
  LCOE: Mean of 5.78 BDT/MWh, with a small standard deviation (0.12 BDT/MWh), indicating minimal variation. Range: 5.63 to 6.02 BDT/MWh.
This shows stable LCOE with some variability in total cost due to uncertainties like weather and demand.
28

## Slide 31
Results
Comparative Analysis
29

## Slide 32
Results
  Our Hybrid System: LCOE of 5.63 BDT/MWh, optimized with large-scale solar, wind, biomass, and battery storage for cost efficiency.
  St. Martin’s Island (Kyushu University, 2021): LCOE of 15.54 BDT/MWh, higher due to smaller scale and resource limitations.
  Pabna Hybrid System (Md. Samiul Islam et al., 2022): Likely higher LCOE, due to smaller scale and lack of large storage.
  Kuakata Off-Grid (Wiley, 2021): Higher LCOE, off-grid nature adds costs.
  Rohingya Refugee System (ResearchGate, 2020): Higher LCOE, similar to other off-grid systems.
  Utility-Scale Solar (BloombergNEF, 2023): LCOE of 6.21–11.44 BDT/MWh, lower but lacks hybrid resilience.
Comparative Analysis
30

## Slide 33
Results
System Reliability
  High Reliability: The reliability curve shows that the system maintains a high probability (close to 1) of meeting load demand, indicating a highly reliable hybrid energy system.
  Minimal Power Shortages: Power shortages are rare, as reflected by the gradual increase in the curve, indicating that shortages occur only at higher power shortage levels (MW).
  Effectiveness of Biomass Backup: Biomass energy effectively mitigates shortages during low solar and wind generation periods, ensuring consistent power supply.
31

## Slide 34
Results
32

## Slide 35
Results
Energy Mix Analysis
  Biomass has the largest contribution to total energy generation.
  PV (Photovoltaic) contributes a smaller portion compared to Biomass and Wind.
  Wind makes up the smallest segment of the total generation.
33

## Slide 36
Results
34

## Slide 37
These are the course outcomes that we have achieved while working on our thesis
Complex Engineering Aspects
35

## Slide 38
Impact Assessment
36

## Slide 39
Impact Assessment
37

## Slide 40
Impact Assessment
38

## Slide 41
Socio-cultural, environmental, and ethical impact
Socio-Cultural
  Enhances electricity access in rural/tribal areas
  Empowers women & marginalized communities
  Boosts education, health & local economy
39

## Slide 42
Socio-cultural, environmental, and ethical impact
Environmental
  Reduces CO₂ and fossil fuel dependence
  Utilizes local solar, wind, biomass resources
  Promotes sustainable and clean energy use
40

## Slide 43
Socio-cultural, environmental, and ethical impact
Ethical
  Promotes energy justice for remote populations
  Supports intergenerational equity
  Aligns with fair, inclusive development goals
41

## Slide 44
Future Improvements
42
Advanced Forecasting Integration
AI driven Energy Management
Grid Integration and Market Participation
Multi-Objective Optimization Objective

## Slide 45
References
[1] Reza, S. E., Nitol, T. A., & Abd-Al-Fattah, I. B. N. E. (2012). Present scenario of renewable energy in Bangladesh and a proposed hybrid system to minimize power crisis in remote areas. International journal of renewable energy research, 2(2), 280-288.
[2] Amiri, M. H., Mehrabi Hashjin, N., Montazeri, M., Mirjalili, S., & Khodadadi, N. (2024). Hippopotamus optimization algorithm: a novel nature-inspired optimization algorithm. Scientific Reports, 14(1), 5032.
[3] Current Status of Renewable Energy Sector in Bangladesh and a Proposed Grid Connected Hybrid Renewable Energy System
[4] Halder, P. K., Paul, N., Joardder, M. U., & Sarker, M. (2015). Energy scarcity and potential of renewable energy in Bangladesh. Renewable and Sustainable Energy Reviews, 51, 1636-1649.
[5] http://www.bpdb.gov.bd/
[6] https://en.wikipedia.org/wiki/Electricity_sector_in_Bangladesh
[7] Hossain, M. A. (2019). Size Optimization of Hybrid Renewable Energy System using Meta-Heuristic Algorithm (Doctoral dissertation, Department of Electrical and Electronic Engineering, Islamic University of Technology, Board Bazar, Gazipur, Bangladesh).
[8] https://energytracker.asia/the-electricity-sector-in-bangladesh-what-comes-next/
43

## Slide 46
[9] SREDA (Sustainable & Renewable Energy Development Authority). (n.d.). Projects / Programs. Retrieved September 28, 2025, from https://ndre.sreda.gov.bd/index.php?id=7
[10] Alam, S. (2024, August 29). How to make Bangladesh’s power sector sustainable. Institute for Energy Economics and Financial Analysis (IEEFA). https://ieefa.org/resources/how-make-bangladeshs-power-sector-sustainable
44